## Slide 1: Put the Center Street Bridge widening forward: about 323,000 vehicle-hours a year saved
Chart: Annual benefit, 2028 AM and PM peak hours re-assigned on each build network (thousand vehicle-hours a year)
| Ferry Street exit ramp | Southport signals and turn lanes | Route 9 auxiliary lane | Center Street Bridge
Vehicle-hours saved a year (thousands) | 37 | 126 | 159 | 323
Center Street saves 323,000 vehicle-hours a year, 8,300 for each million dollars of its USD 38.9 million cost.
The Route 9 auxiliary lane is next at 159,000 (3,400 per million). Re-timed at today's loaded volumes it looks like the biggest saver, but once the 2028 trips re-route, the extra lane at Millbrook only delivers more traffic to the Route 9 bridge, which then sets the queue, and the new Center Street lane draws trips off Route 9 as well.
Southport signals and turn lanes: 126,000 (4,900 per million). Ferry Street exit ramp: 37,000 (2,100 per million).
TDM v4.2 subarea network and 2028 trip tables, user equilibrium to a relative gap below 0.000001. Annual benefit per the TIP scoring guidance: peak-hour savings times 247 weekdays times 2.9. Travel Forecasting Program, 23 October 2026.